## Slide 1: UTAH LAKE C, N, AND P PROJECT

## Slide 2: COMPONENTS
Quantify conceptual models of N and P cycles in Utah Lake
Create external mass balance of C, N, and P for Utah Lake
SedFlux modeling of sediment-water fluxes of nutrients and oxygen

## Slide 3
TP
Main Basin: 0.01-1 mg/L
Provo Bay: 0.05-1 mg/L
PP
0-1 mg/L
Phosphorus model
Sediment
Water
Outflow TP
23-84 tons/yr
TP
Main Basin: 280-1730 mg/kg
Provo Bay: 465-1900 mg/kg
Phytoplankton
0.7-2 % P
TDP
0.003-1 mg/L
DOP
0-0.18 mg/L
PO43+ ≈ SRP
Main Basin: 0.01-0.85 mg/L
Provo Bay: 0.02-4 mg/L
PIP
Zooplankton
0.5-1.6 % P
0.05-160,000 µg/L (small)
50-1,600 µg/L (large)
Fish
1-4.5 % P
0.1-4.5 kg/acre
BD fraction
Fe/Mn compounds
49.1±1.8% (41-61%)
HCl fraction
CaPO4 or acid-soluble organic P
38.6±2.1% (25-47%)
NH4Cl, NaOH, and residual fractions
Loosely bound, exchangeable and organic P, refractory P
12.4%
Confidence
Very high
High
Medium
Low
Very low
Porewater TDP
Main Basin: 1.48 mg/L (0.26-10.82)
Provo Bay: 3.85 mg/L (0.40-6.78)
Dashed boxes are derived from Randall et al. 2019 (PLoS ONE)
External TP Loading
Inflow sources
(streams, WWTPs, drains, springs, groundwater, precipitation)
152-298 tons/yr
Atmospheric Deposition
5.0±3.1 tons/yr
TDP Release
1.7-1.9 ± 0.7-4.0 tons/d
SRP Release
-4.5-27.2 tons/d
Periphyton
Negligible
Macrophytes
0.2-0.6 % P
Macroinvertebrates
5.3-17.0 mg/g dry weight
Uptake
0.1-100 ng/(L*h)
Uptake
0.17-480 µg/(ind.*d)
Uptake not possible to calculate
Excretion, decomp: negligible (periphyton), 0-496 µg/(g dry weight*h) (macroinvertebrates)
Uptake negligible
Excretion
0.01-1,000 µg/(ind.*d)
Excretion, Decomp.
0.1-100 ng/(L*h)
Excretion
Carp: 51.1-117 tons/yr
Uptake not possible to calculate
Excretion, decomp. not possible to calculate
Uptake not possible to calculate
PP settling
192-1,230 tons/y
0-83 tons/d
PP resuspension
173-257 tons/y
0-82 tons/d
Literature-derived values

## Slide 4
TN
0-3000 mg/kg
TN
Main Basin: 0.04-12.4 mg/L
Provo Bay: 0.7-12.4 mg/L
PN
0-0.50 mg/L
Nitrogen model
Sediment
Water
Outflow TDN
367 tons/yr
150-6,847 kg/d
TDN
0.29-5.32 mg/L
DON
0-11.9 (from TKN)
0-1.9 mg/L (from TDN)
DIN
0.01-7.5 mg/L
NO2- + NO3-
0.001-5.2 mg/L
NH3 + NH4+
0.003-5.0 mg/L
Confidence
Very high
High
Medium
Low
Very low
External TN Loading
Inflow sources
(streams, WWTPs, drains, springs, groundwater, precipitation)
2022-2542 tons/yr
Atmospheric Deposition
170 tons/yr
Phytoplankton
5-9 % N
Zooplankton
5-14 % N
0.5-1,400,000 µg/L (small)
500-14,000 µg/L (large)
Fish
8-12 % N
0.8-20 kg/ac
Excretion, Decomp.
10-10,000 ng/(L*h)
TIN Release
-3.8-554.4 tons/d
Ammonia Release
-12.7-554.4 tons/d
Macrophytes
0.8-1.3 % of dry mass
Macroinvertebrates
42.7-141.2 mg/g dry weight
Porewater TDN
0-16 mg/L
Atmospheric N2
Denitrification, anammox
1,372 tons/yr
Water column N fixation
0-4.65 µg/(L*h)
Benthic N fixation
0.1-1.0 tons/h
Uptake
10-10,000 ng/(L*h)
Literature-derived values
Uptake
1.2-2,160 µg/(ind.*d)
Excretion
0.01-10,000 µg/(ind.*d)
Excretion
Carp: 496-1,140 tons/yr
Uptake not possible to calculate
Uptake not possible to calculate
Excretion, decomp. not possible to calculate
Periphyton
Negligible
Excretion, decomp: negligible (periphyton), 0-168 µg/(g dry weight*h) (macroinvertebrates)
Uptake negligible
Uptake not possible to calculate
PN settling
0-130 tons/d
PN resuspension
0-129 tons/d

## Slide 5: EXTERNAL MASS BALANCE
Inputs
Tributaries
Atmosphere
Groundwater
Outputs
Jordan River

## Slide 6: WATERSHEDS
UDWQ sites: orange
WFWQC sites: purple
Facility sites: black
Majority of watershed is monitored  infer unmonitored watersheds from similar monitored watersheds

## Slide 7: WATERSHEDS (NOT TO SCALE)
Most downstream monitoring location(s) used to generate nutrient loads to the lake
Comparing monitored sites with reported WWTP effluent, where appropriate
UDWQ sites: orange
WFWQC sites: purple
Facility sites: black

## Slide 8: C-Q RELATIONSHIPS WATERSHEDS W/O WWTP
Flow x nutrient concentration = nutrient load
Monitored sites are sampled to varying degrees, depending on sampling entity and watershed  use this to inform load estimates